## Slide 1
VLSI MINI PROJECT · RTL/DV SYNOPSIS
Parameterized SPI IP Core
RTL Design, SystemVerilog Verification and FPGA Characterization
Team Mohammad Yasir (1BF24EC078) • Paladugala Ajay Kumar (1BF24EC099) • Palreddigari Navadeep Kumar Reddy (1BF24EC100) • Lokesha NN (1BM25EC424)
Guide Mr. Ajay Kumar D · Assistant Professor
B.M.S. College of Engineering, Bengaluru
Department of Electronics & Communication Engineering
Academic Year 2026–27 · Mini Project
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 2
01 — OVERVIEW
SPI Connects Digital Devices
MASTER / SLAVE PROTOCOL
SPI is synchronous serial communication between a controller and one or more peripherals.
FOUR CORE SIGNALS
SCLK clock · MOSI Master-to-Slave · MISO Slave-to-Master · CS/SS selects the active Slave.
FULL DUPLEX, FOUR MODES
Simultaneous send/receive; CPOL and CPHA define four clocking modes.
WHY PARAMETERIZE
Data width, clock settings and slave configurations should adapt without rewriting the RTL.
MASTER
MOSI
MISO
CS/SS
SCLK
SLAVE 0
SLAVE 1…N
CLOCK MODE STRIP
CPOL + CPHA → Mode 0 | 1 | 2 | 3
Project motivation: Combine configurable RTL, systematic SystemVerilog verification and FPGA characterization in one coherent flow.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 3
02 — PRIOR WORK
Literature Survey
Work | Contribution | Relevance to This Project
Single Master Multiple Slave SPI on FPGA — IEEE ICAEE, 2024 | Verilog multi-slave SPI with FSM control, simulation and FPGA implementation. | Baseline Master/Slave and multi-slave architecture.
Lightweight SPI Master IP for Low Cost FPGAs | Resource-conscious configurable clock, CPOL/CPHA and FPGA resource evaluation. | Motivates parameterization and hardware characterization.
SystemVerilog Verification Environment for SPI Master — ICSP, 2012 | Driver, slave model, scoreboard, assertions, constrained-random tests and coverage. | Supports the structured verification methodology.
General-Purpose SPI Master/Slave IPs on OPB Bus | Configurable technology-independent Master/Slave IP and FPGA implementation. | Established configurable IP approach.
Universal Multiple Devices SPI Interface | Parameterized device selection and multi-device control. | Background for scalable slave selection.
SPI Bus on FPGA Using State Machine Method — JPCS, 2020 | State-machine implementation with SPI timing-mode considerations. | Supports FSM-based RTL and FPGA implementation.
Design and Verification of SPI Bus IP Core — JPCS, 2021 | IP development, structured verification and multiple timing modes. | Supports IP-oriented design and verification.
Observation: These individual techniques are established. This project integrates them into one configurable SPI IP flow and plans systematic FPGA characterization.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 4
03 — WHAT WE’RE SOLVING
Problem Statement & Proposed Solution
PROBLEM
Basic SPI implementations often prioritize functional communication over reusable configuration and systematic validation.
Different data widths, clocks, modes and slave counts
Configuration-dependent FPGA resource and timing effects
Manual waveform inspection alone is insufficient for systematic verification
PROPOSED
One parameterized SPI Master/Slave RTL core with 8 / 16 / 32-bit words, all CPOL/CPHA modes, configurable clock division and 1 / 2 / 4 slaves.
Self-checking SystemVerilog: driver, monitor, scoreboard, assertions, functional coverage, constrained-random testing
Controlled fault injection: sampling edge, bit counter and CS timing
Planned FPGA characterization: LUTs, flip-flops, Fmax, critical path and transfer latency
Design → Verify → Implement → Measure → Analyze
Engineering Question: How do configurable parameters such as data width and slave count affect FPGA resource utilization, timing and performance, while systematic verification ensures correctness across supported SPI modes?
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 5
04A — ARCHITECTURE
Methodology — System Block Diagram
CONTROL / TEST INPUT
SPI MASTER
FSM
Clock Divider
TX Shift Register
RX Shift Register
Bit Counter
Chip-Select Logic
SPI BUS
SCLK
MOSI
MISO
CS
CS0 → Slave0
CS1 → Slave1
CS(N−1) → Slave(N−1)
Configurable slave count: 1 / 2 / 4
PARAMETERS DATA_WIDTH: 8 / 16 / 32 · CPOL: 0 / 1 · CPHA: 0 / 1 · CLK_DIV: configurable · SLAVE_COUNT: 1 / 2 / 4
RTL BUILDING BLOCKS FSM · Shift Registers · Bit Counter · Clock Divider · Chip-Select Logic
Scope boundary: Master and Slave operate in the same FPGA clock domain. Asynchronous CDC between independently clocked domains is outside current scope.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 6
04B — ALGORITHM
Methodology — Transfer Flow & Verification
SPI TRANSFER FLOW
1
START /
LOAD TX DATA
2
ASSERT
SELECTED CS
3
GENERATE
SCLK
4
SHIFT +
SAMPLE DATA
5
BIT COUNTER
REACHES N?
SYSTEMVERILOG VERIFICATION
TEST / DRIVER → DUT → MONITOR → SCOREBOARD → PASS / FAIL
Directed and constrained-random tests; scoreboard checks; assertions; functional coverage.
All four CPOL/CPHA modes; 8 / 16 / 32-bit configurations; reset, back-to-back transfers, 1 / 2 / 4 slaves and data patterns.
CONTROLLED BUG DETECTION
Sampling-edge fault · Bit-counter fault · CS-timing fault
Injected Bug → Verification Failure → Waveform / Assertion Analysis → Root-Cause Identification → RTL Fix → Regression Pass
Goal: systematically verify functional correctness and demonstrate detection of realistic protocol and RTL faults.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 7
05 — TIMELINE
Project Planning
1
SETUP
Week 1–2
SPI study, specification, architecture and interface definition.
2
RTL
Week 3–5
Master, Slave, clock generation, parameterization and initial simulation.
3
VERIFICATION
Week 6–9
Driver, monitor, scoreboard, constrained-random tests, assertions and coverage.
4
FPGA
Week 10–12
Synthesis, implementation, utilization, timing and configuration comparison.
5
RESULTS
Week 13–14
Bug analysis, interpretation, documentation and final presentation.
Execution principles: verification begins with stable RTL blocks; feature freeze precedes FPGA characterization.
Team responsibilities: RTL Design · Verification · FPGA/Characterization · Documentation/Integration. Target: approximately 14 weeks.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 8
06 — BUDGET
Estimated Budget
Sl. No. | Item | Justification | Estimated Cost (INR)
1 | EDA / Simulation Tools | Academic/institutional access assumed | Nil
2 | FPGA Development Board | College/team-provided board assumed | Nil
3 | SPI Peripheral / Components | Optional peripheral, connectors and basic hardware | 500
4 | Report Printing and Binding | Project documentation and submission | 500
5 | Presentation Material | Handouts / supporting printouts | 300
6 | Contingency | Miscellaneous project expenses | 1,200
Total |  |  | ₹2,500
Note: The estimate assumes availability of institutional EDA tools and an FPGA development board. If procurement is required, the budget will be revised accordingly.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 9
07 — REFERENCES
References
A. H. Rahimi, A. K. Halim, A. H. A. Razak, M. F. M. Idros, F. N. Osman, S. A. M. A. Junid and S. L. M. Hassan, “Design and Analysis of Single Master Multiple Slave Serial Peripheral Interface (SPI) on FPGA,” IEEE ICAEE, 2024, DOI: 10.1109/ICAEE62924.2024.10667616.
M. B. Aykenar, G. Soysal and M. Efe, “Design and Implementation of a Lightweight SPI Master IP for Low Cost FPGAs.”
Z. Zhou, Z. Xie, X. Wang and T. Wang, “Development of Verification Environment for SPI Master Interface Using SystemVerilog,” ICSP2012 Proceedings, 2012, DOI: 10.1109/ICoSP.2012.6492015.
“Design and Test of General-Purpose SPI Master/Slave IPs on OPB Bus.”
T. Liu and Y. Wang, “IP Design of Universal Multiple Devices SPI Interface.”
J. Qiang, Y. Gu and G. Chen, “FPGA Implementation of SPI Bus Communication Based on State Machine Method,” Journal of Physics: Conference Series, vol. 1449, 012027, 2020, DOI: 10.1088/1742-6596/1449/1/012027.
D. Wang, J. Yan and Y. Qiao, “Design and Verification of SPI Bus IP Core,” Journal of Physics: Conference Series, vol. 1971, 012032, 2021, DOI: 10.1088/1742-6596/1971/1/012032.
Parameterized SPI IP Core · BMSCE ECE · 2026–27

## Slide 10
THANK YOU
Questions & Discussion
Mohammad Yasir · Paladugula Ajay Kumar · Palreddigari Navadeep Kumar Reddy · Lokesha NN
B.M.S. College of Engineering, Bengaluru
Department of Electronics & Communication Engineering
Guide: Mr. Ajay Kumar D · Assistant Professor
MASTER ─── SCLK ─── MOSI ─── MISO ─── CS ─── SLAVE
Parameterized SPI IP Core · BMSCE ECE · 2026–27